## Slide 1: 20 Years of Bioboost ® - a New Zealand Story of Beneficial Biosolids Re-Use
Graham Morris (NPDC) & Jessica Daly (BECA)
Notes: Intro

## Slide 2
New Plymouth Wastewater Treatment Plant
Notes: Background

## Slide 3
Parameter | Bioboost ®
Production | 1,700T/yr
Size | 2-4mm diameter
Moisture Content | 91% dry solids
Quality | Grade A biosolid
Notes: What is Bioboost?

## Slide 4: How is Bioboost® made?
Raw Material Silo
Mixer
Recycle Silo
Dewatered Sludge (18%DS)
Rotary Drum
End Product Silos (91%DS)
Cooling Screws
Screen
Crusher
Cyclone
Burner
Natural Gas
Hydrogen
Condenser
KO Drum
Biofilter
Notes: How is it made?
Block flow diagram

## Slide 5: Success Factors – Physical Properties
Hard, granular product
2-4mm diameter
Low dust
Organic, slow-release fertiliser – 12-16 week breakdown
Notes: Success Factor #1 – Good product

## Slide 6: Success Factors – Chemical Properties
NPK + trace nutrients
Low heavy metal concentrations
Low pathogen content
Low moisture content – stable if stored in dry conditions
Grade A biosolid standard in NZ
Notes: Success Factor #1 – Good product

## Slide 7: Success Factors
Quality Management – control & consistency of product
Astute Marketing
  Tell the story – beneficial re-use
  Good communication and honesty regarding the product
  Brand champion to market the product
  Treat the product as a valuable commodity
Notes: Success Factor #2 – consistency and quality control of product

## Slide 8: Bioboost’s ® Market
Notes: Bioboost users

## Slide 9: Bioboost ® Next Steps

## Slide 10
Why H2?
NPDC plans to decarbonise
Drum dryer process can be co-fired with NG and H2
Taranaki regional roadmap for green hydrogen
Notes: Why H2?

## Slide 11
Notes: Replacement dryer – currently in the end stages of design.
Enabling works began and were completed last year, with construction of the main dryer hall beginning this year

## Slide 12: Conclusions
Bioboost ® produced for over 20 years
Critical success factors:
  Consistent, high-quality product in terms of physical and chemical properties
  Astute and continued marketing
New dryer co-fired on hydrogen will allow continued 100% beneficial re-use of biosolids for next 20 years
Notes: Process of selection for renewal
Why hydrogen?

## Slide 13: Questions?
Many Thanks to Graham morris Npdc