## Slide 1: Screening-level Waste Life Cycle Assessment
Jingwen Luo
for the identification of environmental hotspots in biosolids processing
Ruth Fisher Tommy Wiedmann
To:

## Slide 2
Mix sludge
Anaerobic digestion
Dewatering
Land
application
Calcium ammonium nitrate, triple superphosphate, potassium chloride
Chart: Contribution to Global Warming Potential (%)
a | -26
b | -4
c | -21
a | 6
b | 13
c | 4
a | 25
Fill in the Blanks
Emission to air
Electricity to grid
Energy
Reject water
Energy
Polymer
Emission to air, soil, water
Fertiliser substitution
Energy
Transportation
Agricultural land
Sandy loam soil under an average Danish precipitation regime
Mechanical dewatering
Treatment of reject water were considered to be the same as for the treatment of wastewater
Mesophilic AD
Process heat is provided by the utilisation of biogas
97 % of biogas is used for electricity production at efficiency of 37.5%
Yoshida et al., (2018) Life cycle assessment of sewage sludge management options including long-term impacts after land application
Land application
Electricity substitution
Fertiliser substitution
Reject water treatment
Transportation
Biosolids processing
Notes: The graph is based on results from a LCA study by Yoshida et al., (2018), an outstanding researcher in the area of applying LCA in biosolids processing. This study is based on data from a large scale WWTP in Greater Copenhagen area, Denmark.

## Slide 3: Background
Preliminary Treatment
Stabilisation
Moisture Removal
Post-treatment
Thickening
Chemical treatment
AD
Aerobic digestion
Lime Stabilisation
Dewatering
Thermal drying
Composting
Thermal technologies
Hydrothermal technologies
Land application
Construction material
Activated carbon
“Waste”
“Resource”
Sustainability Implication ???
Emerging pollutants???
Energy/resource recovery???

## Slide 4: Life cycle assessment
What is LCA ?
Life Cycle Assessment (LCA) quantifies ecological and human health impacts of a product or system over its complete life cycle.
LCA considers diverse environmental impacts from different stages and prevents against “burden shifting”
An updated comprehensive LCA of different biosolids processing options in an Australian context is still lacking
A powerful tool
Research gap

## Slide 5
Mix sludge
Anaerobic digestion
Dewatering
Land
application
Chart: Contribution to Global Warming Potential (%)
a | -26
b | -4
c | -21
a | 6
b | 13
c | 4
a | 25
Fill in the Blanks
Emission to air
Electricity to grid
Energy
Reject water
Energy
Polymer
Emission to air, soil, water
Fertiliser substitution
Energy
Transportation
Land application
Electricity substitution
Transportation
Biosolids processing
LCA
Hidden
Impact
Benefit
Reject water treatment
Reject water treatment
Fertiliser substitution
Notes: The graph is based on results from a LCA study by Yoshida et al., (2018), an outstanding researcher in the area of applying LCA in biosolids processing. This study is based on data from a large scale WWTP in Greater Copenhagen area, Denmark.

## Slide 6: Methodology
Goal and scope definition
Inventory analysis
Impact assessment
Results interpretation
LCA methodology

## Slide 7: Methodology
Goal and scope definition
Inventory analysis
Impact assessment
Functional unit: The processing of 1000 kg of biosolids on a dry matter basis
System boundary: All processes after the thickening up to the final beneficial utilisation or disposal
Data source: Literature data, Ecoinvent database AusLCI database
Software: EASETECH (Environmental Assessment System for Environmental Technologies)
LCIA method: Based on the International Reference Life Cycle Data System (ILCD) handbook
Impact category: Global Warming Potential 100 years (GWP) and Human Toxicity Potential (HT) (cancer effect and non-cancer effect)
Results interpretation

## Slide 8: Methodology
Results interpretation
Sensitivity analysis:
Parameter tested:
Biogas generation rate
Dewater biosolids moisture content
Transportation distance
N2O emission rate after land application
Biosolids Zn content
Methodology:
The sensitivity ratio is calculated as the ratio of the degree of change in the result to the degree of change in the parameter
Maximum and minimum value from literature

## Slide 9: Methodology
Anaerobic digestion
Electricity
Electricity recovery
Dewatering
Land application
T
Emission
GHG/Heavy metal
Anaerobic digestion
Dewatering
Incineration
Landfill
T
Anaerobic digestion
Dewatering
Drying
Pyrolysis
Land application
Electricity
S2
S3
GHG
Fuel
Electricity
Electricity recovery
Electricity
GHG
Emission
Fuel, Electricity
Emission
Fuel
Emission
Electricity
Electricity recovery
GHG
Electricity
T
Emission
Fuel
GHG/Heavy metal
Fertiliser substitution; carbon sequestration
Fuel, Electricity
Fuel, Electricity
Heat recovery from products
Thickened
Biosolids
Thickened
Biosolids
Thickened
Biosolids
Fertiliser substitution; carbon sequestration
S1

## Slide 10: Methodology
Anaerobic digestion
Electricity
Electricity recovery
Dewatering
Land application
T
Emission
GHG/Heavy metal
Electricity
GHG
Fuel
Thickened
Biosolids
Biosolids composition data and the processing flow diagram were taken from an operational study at a secondary WWTP in Sydney
Process data for AD and dewatering were sourced from Alvarez-Gaitan et al. (2016), which used the same case study location.
Mesophilic AD with SRT of 13 days; centrifuge dewatering
C, N, P distribution in the land application stage were sourced from Bruun et al. (2016) based on Danish conditions; urea and monoammonium phosphorus (MAP) were assumed to be displaced
Fertiliser substitution; carbon sequestration
S1

## Slide 11: Data source
Anaerobic digestion
Dewatering
Incineration
Landfill
T
Electricity
Electricity recovery
Electricity
GHG
Emission
Fuel, Electricity
Emission
Fuel
Emission
Thickened
Biosolids
Process data for incineration was based on a full-scale fluidised bed incinerator reported by Yoshida et al. (2018) equipped with electrostatic precipitation, wet scrubbers, and a sludge dryer
The landfill process from EASETECH were used to model the associated environmental impacts
Mass balance and the distribution of heavy metals through incineration were modelled based on data from literature
S2

## Slide 12: Data source
Anaerobic digestion
Dewatering
Drying
Pyrolysis
Land application
Electricity
Electricity recovery
GHG
Electricity
T
Emission
Fuel
GHG/Heavy metal
Fertiliser substitution
Fuel, Electricity
Fuel, Electricity
Heat recovery from products
Thickened
Biosolids
The material balance data for pyrolysis was based on a pyrolysis experiment by Chen et al. (2021) in a tube furnace under 500 °C with a heating rate of 10 ◦C/min and a residence time of 30 min under the final temperature.
The thermal energy consumption during pyrolysis and prior drying was calculated based on empirical equations; the electricity consumption data from an industrial pyrolysis furnace reported in the literature was used
The gaseous and liquid pyrolysis products were assumed to be utilized to offsite heat from natural gas
S3

## Slide 13: Results
Chart: GWP (kgCO2-eq)
| S1 | S2 | S3
GWP | 210.6063 | 277.7411 | 138.8388
Chart: HT-cancer (CTUh)
| S1 | S2 | S3
HT-cancaer | -0.00016983 | 4.9026e-06 | -0.00018456
Chart: HT-non-cancer (CTUh)
| S1 | S2 | S3
HT-noncancer | 0.030805 | 0.00016451 | 0.02499

## Slide 14: Results
Chart: Global Warming Potential (CO2-eq)
| S1 | S2 | S3
AD | 127.2405 | 127.2405 | 127.2405
Biogas leak | 131.4561 | 131.4561 | 131.4561
Biogas utilisation | -350.3198 | -350.3198 | -350.3198
Dewatering | 51.1863 | 51.1863 | 51.1863
Transportation | 125.6184 | 2.5569 | 13.0346
Land application | 288.9368 | -51.611
Fertiliser substitution | -163.512 | -46.6668
Pyrolysis | 109.9152
Py-oil and gas utilisation | -60.9701
Dryer | 215.5738
Incineration | 315.3341
Ash landfill | 0.28693
N2O
CO2
N2O
CO2

## Slide 15: Results
Chart: Human Toxicity potential, cancer effect
| S1 | S2 | S3
land application | 8.0511e-05 | 0 | 6.1232e-05
Fertiliser substitution | -0.00025052 | 0 | -0.00024602
Incineration | 0 | 4.8911e-06 | 0
Others | 1.8007e-07 | 1.1457e-08 | 7.8979e-08
Chart: Human Toxicity potential, non-cancer effect
| S1 | S2 | S3
land application | 0.025867 | 0 | 0.031734
Fertiliser substitution | -0.00088123 | 0 | -0.00095026
Incineration | 0 | 0.00016857 | 0
Others | 3.726e-06 | -4.0624e-06 | 2.0676e-05

## Slide 16: Results
Chart: Sensitivity Ratio
| 0.5 | 1.2 | 1.9 | 2.9 | 3.5999999999999996 | 4.3 | 5.3 | 6 | 6.7 | 7.7 | 8.4 | 9.1 | 10.1 | 10.799999999999999 | 11.499999999999998
 | 2.3942 | 2.5664 | 4.7556 | 1.042 | 0.013521 | 0.043786 | 0.59634 | 0.013521 | 0.043786 | 1.3514 | 0 | 0.61725 | 0.95913 | 6.8753e-05 | 0.99321
Biogas generation rate
Dewatered biosolids solids content
Transportation distance
N2O emission rate for land application
Zn content in biosolids
Some operational parameters can bring large impacts to the assessment results
The importance of some locally relevant parameters cannot be over looked
Chart: GWP of S3 under different biogas generation rate (CO2-eq )
| 150 | 450 | 600
Sum | 579.01 | 138.8388 | -24.577
Chart: GWP of S1 under different N2O emission rate (CO2-eq)
| 1E-4 | 0.95 | 2.4500000000000002
 | -73.9675 | 210.6063 | 654.6695

## Slide 17: Conclusion and Future Perspective
S3 (AD-Pyrolysis-land application) has the best performance compared to other two scenarios in terms of global warming potential and human toxicity cancer effect
Some key operational and locally relevant parameters (e.g. biogas generation rate and N and C balance after land application) can bring large influence to the assessment results
There is a need for collaboration with the industry to refine biosolids processing and composition data as well as studies into land application of biosolids, specifically carbon and nitrogen balance and fertiliser offsets
In future studies, the scope of the assessment will be expanded to include more biosolids processing scenarios, impact indicator, operating conditions; expand system boundary and use Australian specific data

## Slide 18: Acknowledgment
This research is funded by:
ITTC for Transformation of Australia’s Biosolids Resource Project IC190100033
UNSW University International Postgraduate Award (UIPA) scholarship
Petre Foundation scholarship
Thank you for support and advice:
My industry mentor: Joel Edwards - thinkstep-anz

## Slide 19: Thank You !!!