## Slide 1
Enhancing Anaerobic Digestion Performance with the Microbial Hydrolysis Process
David L. Parry, PhD, PE, BCEE
dave.parry@jacobs.com

## Slide 2
Jacobs’ recent research on enhancing anaerobic digestion with the addition of C. bescii.
Where and how did we test MHP using C. bescii?
What were our findings?
How can this be applied at full-scale?
What is the Microbial Hydrolysis Process (MHP) and C. bescii?

## Slide 3
C. bescii is a hyper-thermophilic anaerobic bacteria that is capable of hydrolyzing recalcitrant organic materials.
C. bescii bacteria under a microscope
Caldicellulosiruptor bescii (C. bescii) was isolated in a geothermally heated freshwater pool in Russia in 1990
Thrives at 75°C
Hydrolyzes cellulose and other recalcitrant organic material like waste activated sludge
Data/Figure to support title assertion

## Slide 4
Anaerobic Digestion (AD) enhancement with the Microbial Hydrolysis Process (MHP) using C. bescii bacterium.
Hyper-thermophilic (72-78°C)
Anaerobic
Digestion
MHP
Biogas
Thickened Sludge
Mesophilic (40°C) Thermophilic (55°C)
Biosolids
2-day HRT
VS  VFAs
VFA  Biogas
pH: ~7.0
Notes: Short retention time, flexibility in where it goes in the process train
Improved volatile solids conversion to biogas, reduction in biosolids

## Slide 5
Hyper-thermophilic (75°C)
Anaerobic
Digestion
MHP
More Biogas
Thickened Sludge
Mesophilic (40°C) Thermophilic (55°C)
Less Biosolids
2-day HRT
VS  VFAs
VFA  Biogas
pH: ~7.0
THP
(optional)
MHP is compatible with all AD processes, including the thermal hydrolysis process (THP).
Notes: In Microbial Hydrolysis Process (MHP), C. bescii hydrolyzes volatile solids (VS) and converts VS into volatile fatty acids (VFAs). In the digester, Methanogen Archaea convert VFAs into biogas.

## Slide 6
MHP using C. bescii has been tested at both lab- and pilot-scale.
Lab Scale
10-L Digesters and 5-L Hydrolysis Tanks
Pilot Scale
1200-L Digesters and 500-L Hydrolysis Tank

## Slide 7
MHP was tested using sludge from high-performing digestion systems (>58% Volatile Solids Reduction (VSR))
Facility | Digestion | Existing Performance VSR | Method
Gresham WWTP; Gresham, OR | Mesophilic AD with FOG | 60% | Lab-scale
Encina Wastewater Authority WPCF; Carlsbad, CA | Mesophilic AD | 60% | Lab-scale
Clinton River WRRF, operated by Oakland County WRC; Pontiac, MI | THP Mesophilic AD | 58% | Pilot-scale
Gresham Wastewater Treatment Plant
Portland, OR
Encina Water Pollution Control Facility, Carlsbad, CA
Clinton River Water Resource Recovery Facility
Pontiac, Oakland County, MI

## Slide 8
The lab-scale tests were performed using AnaeroTech anaerobic reactors (model Lobster-i).

## Slide 9
The pilot digestion facility process room contained two anaerobic digester tanks, one MHP tank, and 4 feed holding tanks.
Process Room
Control
Room

## Slide 10
In pilot testing, C. bescii grew approximately 100-fold in 48 hours, for an estimated doubling rate of approximately 6-8 hours in digested sludge.

## Slide 11
M
The primary measurement of AD performance was volatile solids reduction (VSR), calculated by mass balance.
Sludge
Control AD
Test
AD
MHP
Tank
Feed
Tank
Feed
Tank
Data collected:
AD Feed rate
Circulation rate between AD and MHP
  Temperature
  Total solids
  Volatile solids
  Volatile fatty acids
  Alkalinity
  pH
  Ammonia (occasionally)
  Biogas produced (desired)
    Methane
    Hydrogen sulfide
Biogas
Overflow to Drain
Overflow to Drain
Unseeded MHP Tank (lab only)
M
Notes: We had a separate MHP tank on the control at lab-scale that was not seeded

## Slide 12
Adding MHP at the Gresham WWTP increased VSR from 60% in full-scale AD to 80% VSR in the lab-scale AD with MHP.
Chart: Volatile Solids Reduction of Gresham WWTP Sludge at Lab Scale
| 44308 | 44309 | 44310 | 44311 | 44312 | 44313 | 44314 | 44315 | 44316 | 44317 | 44318 | 44319 | 44320 | 44321 | 44322 | 44323 | 44324 | 44325 | 44326 | 44327 | 44328 | 44329 | 44330 | 44331 | 44332 | 44333
CB VSR | 0.63036 | 0.66 | 0.69 | 0.71657 | 0.71924 | 0.66544 | 0.69949 | 0.68986 | 0.68704 | 0.69762 | 0.67317 | 0.76991 | 0.8 | 0.81928 | 0.73527 | 0.74366 | 0.74023
Control VSR | 0.61341 | 0.6 | 0.6 | 0.58848 | 0.56092 | 0.562 | 0.56881 | 0.56865 | 0.58008 | 0.54454 | 0.55386 | 0.699 | 0.72 | 0.71478 | 0.6107 | 0.60399 | 0.59849
Gresham Full-Scale VSR | 0.5061 | 0.6104 | 0.6417 | 0.6423 | 0.6423 | 0.5602 | 0.5724 | 0.5674 | 0.5623 | 0.5753 | 0.6651 | 0.629 | 0.5735 | 0.4963 | 0.5912 | 0.6153 | 0.6706 | 0.6423 | 0.6283 | 0.6426 | 0.6113 | 0.551 | 0.5857 | 0.6756 | 0.6927 | 0.5893 | 0.49534 | 0.60717 | 0.56503 | 0.57907 | 0.59649 | 0.5469 | 0.52143 | 0.62231 | 0.62731 | 0.62695 | 0.6173 | 0.6093

## Slide 13
Adding MHP on digested sludge from Encina WPCF increased VSR from 60% in full-scale AD to 77% in the lab-scale AD with MHP.
Chart: Volatile Solids Reduction of Sludge from Encina WPCF
| 44466 | 44467 | 44468 | 44469 | 44470 | 44471 | 44472 | 44473 | 44474 | 44475 | 44476 | 44477 | 44478 | 44479 | 44480 | 44481 | 44482 | 44483 | 44487 | 44488 | 44489 | 44490 | 44491 | 44492 | 44493 | 44494 | 44495 | 44496 | 44497 | 44498 | 44499 | 44500 | 44501 | 44504 | 44505 | 44508
CB VSR | 0.66413 | 0.68774 | 0.74038 | 0.67769 | 0.68115 | 0.76156 | 0.77165 | 0.77733 | 0.76508 | 0.74613 | 0.75433 | 0.75464 | 0.78047 | 0.77346 | 0.75433 | 0.76792 | 0.77898 | 0.77255
Control VSR | 0.64633 | 0.65891 | 0.70048 | 0.62775 | 0.65537 | 0.7127 | 0.73779 | 0.73055 | 0.70686 | 0.69811 | 0.69153 | 0.70303 | 0.72502 | 0.68137 | 0.72201 | 0.7351 | 0.67982 | 0.70591
Encina WPCF Full-Scale Digester VSR | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6 | 0.6

## Slide 14
Adding MHP to THP-AD at Oakland County, AD increased VSR from 58% in full-scale AD to 75% in the pilot-scale THP-AD with MHP.
Chart: Volatile Solids Reduction of THP Sludge at Oakland County’s Clinton River WRRF

## Slide 15
In summary, the addition of MHP increased anaerobic digestion performance from good VSR (~60%) to great VSR (>75%).
Facility | Digestion | Existing Performance VSR | Method | Control Performance VSR | Test Performance VSR
Gresham WWTP Gresham, OR | Mesophilic AD with FOG | 60% | Lab-scale | 70% Attributed to C. bescii in control | 80%
Encina Wastewater Authority WPCF Carlsbad, CA | Mesophilic AD | 60% | Lab-scale | 71% Attributed to long retention time | 77%
Clinton River WRRF, operated by Oakland County WRC; Pontiac, MI | THP Mesophilic AD | 58% | Pilot-scale | 65% Attributed to solids settling in control | 75%
Notes: The control “kept us honest”. While we did see some improved digestion in the control digesters without intentional addition of MHP C. bescii, there was an explanation for the improved performance for each. Even still, addition of MHP outperformed the control and full-scale digesters.

## Slide 16
At Gresham, MHP with recuperative thickening can be added to enhance digestion capacity and performance.
MHP with recuperative thickening.

## Slide 17
Encina plans to implement MHP in the future based on successful lab and future pilot tests.
Mesophilic Anaerobic Digesters 4-6
Class A Biosolids
Centrate
Dewatering
Microbial Hydrolysis Process Tanks 1-3
2
3
1
4
5
6
Thickened Primary
& Waste Activated Sludge
Biogas
Biogas
Biogas
2
Digested Sludge
Storage Tank
Recuperative Thickening
Heat Recovery
Centrate
Integrated Biosolids Dryer/Pyrolyzer/Gasifier

## Slide 18
Oakland County piloted MHP to evaluate the potential improvement in performance to their THP AD process.

## Slide 19: Clinton River WRRF Oakland County Pontiac, MI
Biogas Treatment
THP
Primary
Digester
Secondary
Digester
Pre-Dewatering
Post-Dewatering
Biosolids
Steam
Sludge
Electricity
Buildings
Natural Gas
Biogas
Flare
MHP Tank
Standpipe
Standpipe
Notes: By adding MHP, Oakland County could increase their biogas production by 30 percent and reduce their biosolids production by 25 percent.

## Slide 20: VCS Denmark Ejby Molle WRRF
500,000 population equivalent
Achieved Energy Neutrality through technology and business strategy

## Slide 21: Microbial Hydrolysis Process at EJWRRF

## Slide 22
For a conventional AD system at a 300,000 PE WRRF:
Applying MHP can result in a total value of 450,000 $/yr
Anaerobic
Digestion
MHP
40% More Biogas 180,000 $/yr
Thickened Sludge
30% Less Biosolids
270,000 $/yr Value
TS: 15 dry tonnes per day
VS/TS: 78%
TS: 8.9 dry tonnes/day w/o MHP
TS: 6.5 dry tonnes/day with MHP
Biogas w/o MHP: 340 m3/h (200 scfm)
Biogas with MHP: 480 m3/h (280 scfm)
VSR: 55% w/o MHP
VSR: 75% with MHP
Notes: $80/dry tonne savings

## Slide 23
MHP can be added to any digestion process to enhance anaerobic digestion performance and decrease operating costs.
Increase VSR of over 75%
Increased Biogas Production
Decreased Biosolids Production
Anaerobic
Digestion
MHP
More Biogas
Thickened Sludge
Less Biosolids

## Slide 24
Enhancing Anaerobic Digestion Performance with the Microbial Hydrolysis Process
Questions?
David Parry, PhD, PE, BCEE
dave.parry@jacobs.com