## Slide 1
Beneficial Use of Organic Materials to Land
What is Changing?
Nick Walmsley

## Slide 2
THE NEW GUIDE
What will it do?
Purpose
Develop a framework that deals consistently with organic materials
Recognise commonalities of nutrients, contaminants and end use
Takes an integrated approach with quality criteria to protect both the environment and public health
What Will it Supersede?:
2003 Biosolids Guidelines
References to 2003 Biosolids Guidelines in:
  NZS 4454 – Composts, soil Conditioners and Mulches
  Regional Plans, Bylaws, some agricultural guides, consent conditions?
Notes: Hopefully a better informed and level playing field

## Slide 3
THE NEW GUIDE
Steering Group
Auckland Council and WasteMinz Organic Material Sector Group; George Fietje
Centre for Integrated Biowaste Research and ESR Limited; Jacqui Horswell
Greater Wellington Regional Council; Paul Bruce
Ministry for the Environment; Nigel Clarke
Ministry of Health; John Harding
Ministry for Primary Industries; Andrew Pearson
NZ Land Treatment Collective and Lowe Environmental Impact; Katie Beecroft
Water New Zealand; Nick Walmsley

## Slide 4
BACKGROUND
NZ Biosolids Guidelines 2003
Defined biosolids as any product that included WWTP sludge and met quality standards
Included soil replacement quality standards
Did not consider non-biosolids quality to land
Tighter default limits from 2013
Expected to be reviewed within 5 years i.e. by 2008
Notes: Review didn’t happen and more science now available.
Lots of concern around the industry re 2013 limits but limited interest at central government for change.
Eventually managed to it off the ground through an accumulation of funds for a wider scope.

## Slide 5
ISSUES
The Benefits
Unlike other waste materials, good prospects exist for alternative, beneficial end-use options for organic material if well managed
To fit the criteria of “beneficial re-use” specified in the Guide the organic material must benefit soil biological, chemical or physical properties
There has been substantial increase in scientific knowledge in recent years and communities are increasingly interested in sustainable waste management
Note: all organic wastes contain pathogens and other contaminants
Notes: Sustainable management of organic wastes is important as >60% of landfill stream – literally a waste!
Current trends are for more varying mixtures of organic materials used to create energy. Why set rules that are only applicable to one material type?
Inorganic and synthetic fertilisers have increasing costs
We are running out of Phosphorous
We still want to increase land productivity

## Slide 6
SCOPE
What Raw Organic Materials are Covered?
Household organics (food waste, green waste)
Paper and cardboard
Primary sector related organic waste (e.g. agricultural wastes, meat wastes)
Manures
Sewage sludge
Pulp and paper waste
Biodegradable nappies and sanitary items
Notes: Lots of debate re the last item, especially as all the materials may not be degradable. Composting most popular process.

## Slide 7
SCOPE
What has changed?
Simpler, less grades to comply with
No soil limits or mass load calculation
Nitrogen loading as primary control
Pathogens;
  Same list with enteric virus replaced by human adenovirus
  Less verification samples required
Inorganics;
  Same contaminants and old ‘b’ grade limits
Organics;
  No old historical compounds e.g. dioxins
  New compounds representing EOCs
Notes: Salmonella testing improved
7 Vs 15 samples as per WA guide 2012

## Slide 8
QUALITY CRITERIA
Product Standards
Stabilisation Grade A (Type 1) could have a Permitted Activity planning control *
Grade B (Type 2) could have a Controlled Activity planning control*
Grade A or B material which is non-compliant for contaminants (Type 3) should be reused under a specific resource consent or safely disposed
*if applied according to the requirements of this Guide
Type | Stabilisation Grade | Contaminant Grade
1 | A | Compliant
2 | B | Compliant
3 | A or B | Non-compliant
Notes: Stabilisation Grade ‘A’ (Type 1) is one in which pathogens and vector-attracting compounds, such as volatile solids, have been substantially reduced or removed
To achieve stabilisation Grade B, the product needs to meet a lesser degree of stabilisation plus one of the VAR requirements specified

## Slide 9
CONTROLS
Nitrogen Loadings
For continual application ≤ average of 200 Kg N/Ha/year over up to two years,
  based on evidence that the organic nitrogen is eventually mineralised.
  additional applications should be based on a site specific site and crop assessment (e.g. nutrient management plan)
Applications to rebuild degraded soil or to refurbish contaminated land should be limited to an application of 150 kg mineral N/Ha.
Plus soil incorporation and similar management controls to NZ Biosolids Guidelines
Notes: Up to 3 years currently used e.g. Nelson but under specific consent conditions

## Slide 10
QUALITY CRITERIA
Pathogens
Pathogen | Standard
Verification Sampling: | 
E. Coli | less than 100 MPN/g
Campylobacter | less than 1/25g
Salmonella | less than <2 MPN/g (< 1/25g)
human adenovirus | less than 1 PFU/0.25g ………………...(enteric viruses < 1 PFU/4g)
helminth ova | less than 1/4g
Routine Sampling: | 
E. coli | less than 100 MPN/g
Notes: Brackets are previous values.

## Slide 11
QUALITY CRITERIA
Stabilisation Grade Sampling Frequencies
Grade | Monitoring type | Sampling regime | Parameters to be monitored
A | Product verification |  7 evenly dispersed grab samples per month for a 3-month period with  3 failures. If > 3 failures then the 7 following consecutive grab samples must comply. | E. coli Salmonella Campylobacter human adenovirus helminth ova VAR
 | Routine sampling |  1 grab sample per week | E. coli VAR
B | Product verification | N/A for pathogen testing | VAR
 | Routine sampling | N/A for pathogen testing | VAR
Notes: The number of verification samples has been reduced from 15 in the Guidelines for the Safe Application of Biosolids to Land in New Zealand, 2003, to 7 samples which is in line with the Western Australian guidelines for biosolids management (2012)

## Slide 12
QUALITY CRITERIA
Inorganic Contaminants
Parameter | Concentration limit (mg/kg dry weight)
Arsenic | 30
Cadmium | 10
Chromium | 1500
Copper | 1250
Lead | 300
Mercury | 7.5
Nickel | 135
Zinc | 1500
Notes: All values are the existing ‘b’ grade values
1. Sampling methods are to comply with those specified in this guide
2. All values are to be 95th percentiles from the data set
3. No individual value from the data set shall exceed the limits by more than 20%
Refer Envirolink re soil levels and confusion.

## Slide 13
QUALITY CRITERIA
Organic Contaminants
Parameter | Concentration limit (mg/kg dry weight)
Perfluoro compounds (PFOS and PFOA) | 0.01
Absorbable organic halogens (AOX) | 450
Polycyclic aromatic hydrocarbons (PAH sum) | 5
Nonyl phenol and ethoxylates (NP/NPE) | 25
Phthalate (DEHP) | 75
Linear alkydbenzene sulphonates (LAS) | 1500
Musks – Tonalide | 15
Musks – Galaxolid | 10
Notes: Non of the existing organics based on banned substances remain. The organic contaminants in Table 4.2 of the NZ guidelines are considered obsolete in view of the on-going research findings on their sources and fate in New Zealand;
New contaminants should be considered for inclusion in view of recent findings on the levels and risk potential of EOCs in biosolids. Based on local and international literature, EOC classes should include endocrine disruptors, flame retardants, antimicrobial agent and pharmaceuticals; persistent herbicide (clopyralid); cleaning agent
At this stage, there is not enough information to derive New Zealand specific limits but interim values used from current EU guidance on organic pollutants for sludge used in agriculture, compost and digestates
1. Sampling methods are to comply with those specified in this guide
2. All values are to be 95th percentiles from the data set
3. No individual value from the data set shall exceed the limits by more than 20%

## Slide 14
FORMAT OF THE GUIDE
Volume 1 – the Guide
Similar management controls to previous
Similar pathogen and inorganic contaminants
Totally new organic contaminants to be measured;
  No longer measure banned substances e.g. Dioxins
  Measures compounds representative of emerging organics e.g. Herbicides, antibacterials, fungicides
No soil replacement standards
Nitrogen loading limits as control
Volume 2 – Technical Support Information
Technical reports supporting proposed limits, consultation advice, legislation summary,

## Slide 15
PROGRAMME
Timing of Development
Public draft issued shortly
Open invitation for comments
Open workshops
Meetings with specific stakeholders, particularly those for agricultural industry groups
Publish end 2016/ early 2017?